## Slide 1: ManureDB: Building a Nationwide Manure Test Database
Nancy Bohl Bormann
PhD Candidate - University of Minnesota
bohlb001@umn.edu @nlbb
MASTPAWG 2023
2/22/2023

## Slide 2: Overview
Manure provides nutrients for cropping systems.
Current published livestock manure “book values” (the approximate manure nutrient concentrations) used in the United States (U.S.) are several decades old.
Recent data from several Midwest U.S. labs indicated manure nutrient data has changed compared to published Midwest Plan Service (MWPS) manure book values (2004).
The University of Minnesota has grant funding to create a manure nutrient database called ManureDB to update these values.
We are partnering with laboratories that analyze manure.

## Slide 3: What are manure book values used for?
Developing manure management plans
Designing manure storages
Establishing best management practices for manure land application
Modeling nutrient cycling and gas emissions
Notes: Organic fertilizer containing essential plant nutrients
Non-homogeneous product
Like commercial fertilizers, need to be aware of the environmental risk of losing nitrogen (N) and/or phosphorus (P)

## Slide 4: Preliminary Lab Data
Three Midwestern laboratories
  Over 80,000 samples!
Samples from 2012-2021
Sorted between liquid and solid
Divided into four main
livestock groups
  Beef
  Dairy
  Poultry
  Swine
Notes: Lab results and book values had various units converted into:
      lbs of nutrient/ton for solid manure
      lbs of nutrient/1000 gallons for liquid manure
Calculated medians of total nitrogen, NH4-N, P2O5, and K2O analyses
No differentiations for most of these samples of:
  Housing
  Manure storage
  Age

## Slide 5: Comparing MWPS to 3 Labs - Dairy Liquid Manure
NH4-N
P2O5
K2O
Total N
Notes: Dairy TN – lower
NH4-N -higher
P lower
K lower

## Slide 6: Comparing MWPS to 3 Labs - Poultry Solid Manure
NH4-N
P2O5
K2O
Total N

## Slide 7: Takeaway from this preliminary study
Preliminary data from 3 labs showed changes in manure trends from published manure book values
Detailed metadata will be key for future robust comparisons
Notes: Proving what many had long suspected….

## Slide 8
Most samples had minimal descriptions beyond animal species and little is known about storage types
                Age
                Nutrition
                Housing
                Manure Handling and Treatment
                Storage

## Slide 9: ManureDB: Nationwide Manure Test Database
-Minnesota Supercomputing Institute
-Stakeholder group
-Schema
-Database
-Website
-Laboratory cooperation
-Currently cleaning and uploading data
-Over 58,000 samples in the database with more getting processed for entry
Notes: Bigger than a spreadsheet

## Slide 10: Project Team
Commercial manure laboratories
Ag professionals
Researchers
Engineers
Regulatory & agency staff
Livestock commodity groups
Alternative energy groups

## Slide 11: Data Use Agreement & Privacy Concerns
Two-page agreement between the University of Minnesota and participating laboratory
No customer names or addresses
Only first 3 digits of the ZIP code will be imported into the database
ZIP codes and laboratory identities will not be included in the Public Facing Database
At least four samples will be needed to publicly show up in summaries

## Slide 12: Schema

## Slide 13: Survey Data Template
Lab Name
Year Analyzed (required)
Date Sampled, Date Received, Date Analyzed, Date Reported
Sample ID, Account #
ZIP Code, State
Sample Notes
Manure Type
Animal or Other Amendment Type
Manure Treatment
Agitated
Bedding Included
Storage Type
Length of Storage
Application Method
Targeted Analytes

## Slide 14: Manure Type
Liquid
Slurry
Semi-solid
Solid
Separated Solid
Digestate
Runoff
Sludge
As-excreted (urine)
As-excreted (feces)
Litter
Compost
Unknown

## Slide 15: Manure Treatment
No Treatment
Alum
KLASP
Phytase
PLT
Poultry Guard
Other Treatment
Unknown

## Slide 16: Agitated?
Yes
No
Unknown
Bedding Type
Hardwood Sawdust
Hardwood Shavings
Peanut Hulls
Pine Sawdust
Pine Shavings
Rice Hulls
Sand
Straw
Not Included
Other/Unspecified Bedding
Unknown
Length of Storage?
Daily haul
0 to <3 months
3 to <6 months
6 to <12 months
12+ months

## Slide 17: Animal or Other Amendment Type
Alpaca
Bat
Beef - Breeding
Beef - Calf
Beef - Replacement Heifers
Beef - Stocker
Beef
Biosolids
Bison
Cattle
Chicken
Chicken - Breeder
Chicken - Broiler
Chicken - Layer
Chicken - Pullet
Dairy - Calf
Dairy - Calf and Heifer
Dairy - Heifers
Dairy - Lactating Cow
Dairy - Dry Cow
Dairy
Deer
Donkey
Duck
Elephant
Elk
Emu
Ferret
Fish
Geese
Goat
Guinea Pig
Horse
Llama
Mink
Mouse
Partridge
Pigeon
Poultry
Rabbit
Rat
Quail
Sheep
Swine - Farrow to Wean
Swine - Farrow to Feeder
Swine - Farrow to Finish
Swine - Feeder to Finish
Swine - Finisher
Swine – Gestation
Swine - Wean to Finish
Swine - Nursery
Swine - Boar Stud
Swine
Turkey
Turkey - Meat
Turkey - Hen
Veal
Worm
Other - Egg Wash Water
Other - Fish Pond Sludge
Other – Grape Pomace
Other - Mushroom
Other - Paunch
Other - Sewage Sludge
Other - Truck Wash
Mixed
Unknown

## Slide 18: Storage Type
Lagoon
Uncovered Pit or Tank
Covered Pit or Tank
Earthen Basin
Runoff Holding Pond
Solid
Underfloor Solid Storage
Stockpiled Under Cover
Stockpiled Outdoors
Cage-free Poultry
Unknown
Application Method
Irrigation
Broadcast
Broadcast - Incorporated within 24 hours
Broadcast - Incorporated after 24 hours
Injection
Unknown

## Slide 19: Targeted Analytes
Moisture
Total Nitrogen
Phosphorus
Water Extractable Phosphorus
Potassium
Soluble Potassium
Zinc
Sulfur
Total Carbon
Total Organic Carbon
pH
Volatile Solids
Total Suspended Solids
Nitrate-N
Chloride
Ash
Total Solids
Electrical Conductivity
Organic Matter
Carbon:Nitrogen Ratio
Ammonium-N
Boron
Calcium
Copper
Iron
Magnesium
Manganese
Molybdenum
Sodium
Arsenic
Cadmium
Cobalt
Chromium
Mercury
Nickel
Lead
Selenium
Aluminum
Barium
Silicon
Strontium
Calcium Carbonate Equivalent (CCE)
Sodium Absorption Ratio (SAR)
Cation Ratio of Soil Structural Stability (CROSS)
Fecal Starch
Notes: Recommended methods of manure Analysis

## Slide 20: Choose Method, Basis, Units
Methods options based on:
  Recommended Methods of Manure Analysis
  AgGateway Modus Agronomic Testing Lab Standard (currently updating!)
  Interviews with labs
Basis
  As received (wet)
  Dry
Units
  %
  ppm
  lbs/1000 gal
  lbs/ton

## Slide 21: Spreadsheet Validation
Checks that all the parameters are consistent
Columns need to be cleaned up or edited
Once it passes, we can upload to the database

## Slide 23: Future Plans
Finish construction and user-testing of ManureDB beta site in collaboration with participating laboratories
Publish ManureDB as a publicly available website
Continue to recruit more laboratories to participate in the database
Notes: ManureDB website:
http://manuredb.umn.edu
Ag Data Commons

## Slide 24: What are the steps to get data in ManureDB?
Contact me or manure@umn.edu
We can set up an initial meeting to learn more about the manure database project and your laboratory
Send out the data use agreement for signatures
Once signed by the lab, U of M will sign and return the fully executed agreement
We can meet again to review the lab’s methods, analytes, column names if needed
Send a spreadsheet of your lab’s data, as far back as you wish to go
We work through the spreadsheet validation process and may have a few questions for the lab as we go
Import into ManureDB!

## Slide 25
Stay in the loop!
Interested in learning more?
  manure@umn.edu
  z.umn.edu/
  ManureDB-signup
ManureDB is supported through USDA NIFA Award 2020-67021-32465.

## Slide 26: Acknowledgements
Additional Authors:
Melissa L. Wilson, Associate Professor, University of Minnesota
Erin L. Cortus, Associate Professor and Extension Engineer, University of Minnesota
Kevin Janni, Extension Engineer, University of Minnesota
Larry Gunderson, Pesticide & Fertilizer Management, Minnesota Department of Agriculture
Kevin Silverstein, Scientific Lead RIS Informatics Analyst, University of Minnesota
This work is supported by the AFRI Foundational and Applied Science Program [grant no. 2020-67021-32465] from the USDA National Institute of Food and Agriculture, the University of Minnesota College of Food, Agricultural and Natural Resource Sciences, and the Minnesota Supercomputing Institute.

## Slide 28: Comparing MWPS to 3 Labs - Swine Liquid Manure
NH4-N
P2O5
K2O
Total N
Notes: With differences in swine age and housing, wide variety of values and the 3 lab medians were within the MWPS ranges

## Slide 29: Comparing MWPS to 3 Labs - Beef Liquid Manure
NH4-N
P2O5
K2O
Total N

## Slide 30: Comparing MWPS to 3 Labs - Poultry Liquid Manure
NH4-N
P2O5
K2O
Total N
Notes: N – higher

## Slide 31: Comparing MWPS to 3 Labs - Swine Solid Manure
NH4-N
P2O5
K2O
Total N

## Slide 32: Comparing MWPS to 3 Labs - Dairy Solid Manure
K2O
NH4-N
P2O5
Total N

## Slide 33: Comparing MWPS to 3 Labs - Beef Solid Manure
NH4-N
P2O5
K2O
Total N

## Slide 34
Liquid | Total N | NH4-N | P2O5 | K2O
Swine | o | o | - | +
Dairy | - | o | - | o
Beef | o | o | o | o
Poultry | o | + | - | +
Liquid Manure sample trends 2012-2021 compared to MWPS/ASABE manure book values.
(+) = trending higher
(o) = no change/conflicting samples
(-) = trending lower
Notes: Wilson photos

## Slide 35: Dairy Liquid N
Livestock Type | Total N
MWPS | lbs/1000 gal of manure
Dairy Cow | 31
Dairy Heifer | 32
Dairy Calf | 27
Dairy Herd | 31
ASABE | 
Dairy lagoon effluent | 6
Dairy slurry | 25
3 Midwest labs | 
Dairy | 20
1 East lab | 
Dairy | 24
Notes: 3 lab 10869 samples
East lab 528 samples

## Slide 36: Dairy Liquid P
Livestock Type | P2O5
MWPS | lbs/1000 gal of manure
Dairy Cow | 15
Dairy Heifer | 14
Dairy Calf | 14
Dairy Herd | 15
ASABE | 
Dairy lagoon effluent | 3
Dairy slurry | 25
3 Midwest labs | 
Dairy | 9
1 East lab | 
Dairy | 9
Notes: 3 Midwest labs 10,869 samples
1 eastern lab 528 samples

## Slide 37: Swine Liquid P
Livestock Type | P2O5
MWPS | lbs/1000 gal of manure
Swine Farrowing | 12
Swine Nursery | 19
Swine Grow-Finish (deep pit) | 42
Swine Grow-Finish (wet/dry feeder) | 44
Swine Grow-Finish (earthen pit) | 22
Swine Breeding-Gestation | 25
Swine Farrow-Finish | 24
Swine Farrow-Feeder | 18
ASABE | 
Swine Finisher, slurry, wet-dry feeders | 18
Swine slurry storage -dry feeders | 34
Swine flush building | 13
Swine agitated solids and water | 11
Swine lagoon surface water | 4
Swine lagoon sludge | 48
Livestock Type | P2O5
 | lbs/1000 gal of manure
3 Midwest labs | 
Swine | 22
1 East lab | 
Swine | 10
1 SE lab | 
Swine-lagoon | 0.71
Notes: 3 labs 49K
1 east lab 369

## Slide 38: Swine Liquid K
Livestock Type | K2O
MWPS | lbs/1000 gal of manure
Swine Farrowing | 11
Swine Nursery | 22
Swine Grow-Finish (deep pit) | 30
Swine Grow-Finish (wet/dry feeder) | 40
Swine Grow-Finish (earthen pit) | 20
Swine Breeding-Gestation | 24
Swine Farrow-Finish | 23
Swine Farrow-Feeder | 19
ASABE | 
Swine Finisher, slurry, wet-dry feeders | 20
Swine slurry storage -dry feeders | 24
Swine flush building | 17
Swine agitated solids and water | 6
Swine lagoon surface water | 7
Swine lagoon sludge | 7
Livestock Type | K2O
 | lbs/1000 gal of manure
3 Midwest labs | 
Swine | 32
1 East lab | 
Swine | 17
1 SE lab | 
Swine-lagoon | 5.5
Notes: 3 labs 49k
E lab 369
SE lab 44k

## Slide 39: Poultry Liquid P
Livestock Type | P2O5
MWPS | lbs/1000 gal of manure
Broilers | 40
Pullets | 35
Layers | 52
Tom Turkeys | 40
Hen Turkeys | 38
3 Midwest labs | 
Poultry | 29
Notes: 3 Midwest labs 225 samples

## Slide 40: Poultry Liquid K
Livestock Type | K2O
MWPS | lbs/1000 gal of manure
Broilers | 29
Pullets | 30
Layers | 33
Tom Turkeys | 29
Hen Turkeys | 32
3 Midwest labs | 
Poultry | 35
Notes: 3 Midwest labs 225 samples

## Slide 41: Future Plans
Standardize fields for the future incoming samples
    Location, manure type, agitation, species, bedding, storage type, and analytical method
Create a unit conversion mechanism for data uploads
Recruit more laboratories to participate in the ManureDB project
Compare and analyze more data, especially more detailed data for each species
Design ManureDB with statistical and data visualization features for future public use

## Slide 42
Solid | Total N | NH4-N | P2O5 | K2O
Swine | + | o | + | +
Dairy | o | o | o | +
Beef | + | - | + | +
Poultry | + | o | o | +
Solid manure sample trends 2012-2021 compared to MWPS/ASABE manure book values.
(+) = trending higher
(o) = no change/conflicting samples
(-) = trending lower
Notes: Wilson solid manure photo

## Slide 43: Poultry Solid K
Livestock Type | K2O
MWPS | lbs/ton of manure
Broilers | 36
Pullets | 27
Layers | 26
Tom Turkeys | 30
Hen Turkeys | 30
ASABE | 
Poultry Leghorn Pullets | 27
Poultry Leghorn Hen | 31
Poultry Broiler Litter | 33
Poultry Turkey Litter | 30
3 Midwest labs | 
Poultry | 37
1 East lab | 
Poultry | 40
Notes: 3 MW labs – 9338 samples
1 E lab -1001 samples

## Slide 44: Swine Solid N
Livestock Type | Total N
MWPS | lbs/ton of manure
Swine Farrowing | 14
Swine Nursery | 13
Swine Grow-Finish | 16
Swine Breeding-Gestation | 9
Swine Feeder Pig | 10
Swine Farrow-Finish | 14
3 Midwest labs | 
Swine | 16
1 East lab | 
Swine | 18
Notes: 3 Midwest labs -356 samples
East lab – 75 samples

## Slide 45: Swine Solid P
Livestock Type | P2O5
MWPS | lbs/ton of manure
Swine Farrowing | 6
Swine Nursery | 8
Swine Grow-Finish | 9
Swine Breeding-Gestation | 7
Swine Feeder Pig | 7
Swine Farrow-Finish | 8
3 Midwest labs | 
Swine | 18
1 East lab | 
Swine | 20
Notes: 3 Midwest labs -356 samples
East lab – 75 samples

## Slide 46: Swine Solid K
Livestock Type | K2O
MWPS | lbs/ton of manure
Swine Farrowing | 4
Swine Nursery | 4
Swine Grow-Finish | 5
Swine Breeding-Gestation | 5
Swine Feeder Pig | 4
Swine Farrow-Finish | 5
3 Midwest labs | 
Swine | 7
1 East lab | 
Swine | 9
Notes: 3 Midwest labs -356 samples
East lab – 75 samples

## Slide 47: Poultry Solid N
Livestock Type | Total N
MWPS | lbs/ton of manure
Broilers | 46
Pullets | 48
Layers | 34
Tom Turkeys | 40
Hen Turkeys | 40
ASABE | 
Poultry Leghorn Pullets | 43
Poultry Leghorn Hen | 37
Poultry Broiler Litter | 75
Poultry Turkey Litter | 44
3 Midwest labs | 
Poultry | 53
1 East lab | 
Poultry | 52
Notes: 3 MW labs – 9338 samples
1 E lab -1001 samples